Cabin
 - canopy secure, clean
 - controls unlocked, seat belts
 - flight manual tech log, airworthiness cert, radio licence
 - compass & card
 - emergency equipment, ELT
 - controls & trim free
 - mags. Off, throttle closed
 - fuel valve on, tank selected
 - master on, lights on, walk around, check lights & stall warning
 - lights off
 - fuel pump on, check pressure, pump off
 - master off

Right Wing
 - flap secure
 - aileron free movement
 - surfaces clean
 - free of damage
 - remove tie-downs, chocks
 - main gear undamaged, tyre tread, brakes, oleo extension, spats secure
 - check fuel drain

Nose
 - cowl flap, check oil >4qts
 - cowl secure
 - exhaust secure
 - windscreen clean
 - nose wheel undamaged, tyre tread, oleo 50-80mm, spats secure
 - air intakes clear
 - prop & spinner clean
 - alternator belt tight
 - check cowling fuel drain

Left Wing
 - check fuel drain
 - pitot tube clear
 - main gear undamaged, tyre tread, brakes, oleo extension, spats secure
 - surfaces clean
 - free of damage
 - remove tie-downs, chocks
 - aileron free movement
 - flap secure

Empennage
 - fuel quantity, endurance
 - fuel cap locked
 - fuel drain – clear, no water, no dirt
 - left static vent clear
 - horizontal stabiliser free movement, surface clean
 - rudder movement, surface clean
 - tail section screws & cables
 - luggage door closed

Passenger Briefing
 - Emergency equipment location & use : ELT, extinguisher, first aid, axe
 - Outside : keep behind wings, clear of prop
 - Cabin entry & exit
 - Canopy emergency release
 - Headset, use of radio push to talk
 - Stowage pockets, airsick bags
 - Seats, belts (always secure)
 - Keep clear of controls – stick, rudder
 - Lifejacket use if equipped
 - Assist with traffic lookout
 - Notify pilot of dizziness, nausea, toilet, etc.

Engine Start
 - parking brake set
 - seat belts fastened
 - check circuit breakers
 - avionics switch off
 - mixture full rich
 - carb heat off
 - throttle full movement, set ¼” open
 - prime as required
 - fuel on lowest tank
 - master on
 - fuel pump on, check pressure
 - clear area
 - start with mag switch
 - throttle 1200 rpm
 - oil pressure positive
 - check instruments
 - fuel pump off

After Start
 - avionics on
 - lights on
 - set & check radio
 - transponder standby, check code
 - release brake for taxi

Run-Up
 - parking brake set
 - fuel pump on
 - select other tank (fullest)
 - mixture full rich
 - check Ts & Ps
 - throttle 2000rpm
 - carb heat check : min drop 20rpm, max 200rpm
 - mag check : max drop 175 rpm, diff. 50Rpm
 - vacuum/suction gauge
 - ammeter
 - throttle idle – 600-700rpm
 - release brake & taxi to holding point

Take-off
Holding point checks:
  TMPFFIHCTR
Line-up checks:
 RTLWDR
Full throttle, keep straight
Rotate 55 kts
Best angle climb 64 kts
Clean-up – flaps, fuel pump
Best rate climb 74 kts

Max Performance Take-off
Holding point checks
  TMPFFIHCTR
Note +ve acceleration point
Note rotate point
Line-up checks
 RTLWDR
Hold brakes
Throttle 2000rpm
Cycle Carb heat
Full throttle, min 2300rpm
Release brakes, keep straight
Begin Rotate 55kts
Best angle climb 64 kts
Clean-up – flaps, fuel pump
Best rate climb 74 kts

Cruise, Climb
Cruise 2400-2450rpm
Approx 90 kts

Approach, Landing
Downwind checks
 BUMFHW
Carb. Heat On
Throttle 1800rpm
Check white arc
Flaps 10, lookout, turn base
Throttle as required
Speed 75 kts
Turn Final
Full flaps 35
Speed 63 kts
Short final : carb heat off

Precision Landing
Downwind checks
 BUMFHW
Pick touch-down point, identify short finals area
Carb. Heat On
Throttle 1800rpm
Check white arc
Flaps 10, lookout, turn base
Throttle as required
Flaps 20
Speed 70 kts
Turn Final
Full flaps 35°, 64 kts
Short final : carb heat off

Speeds
Stall, full flap (Vs0)	47 kts
Stall, clean (Vs1)	53 kts
Take-off rotate	55 kts
Best angle climb	64 kts
Best rate climb	74 kts
Normal climb	90 kts
Normal Cruise (Vno)	126 kts
Best glide distance	75 kts
Approach	74 kts
Final	64 kts
Precision Landing	64 kts
Max flap (Vfe)	103 kts
Max Manoev. (Va) 88-111 kts
Never exceed (Vne)	160 kts

Max crosswind	17 kts

Transponder Codes
xxxx – Aircraft discreet code
yyyy – Flight plan assigned code
1400 – Local Circuit VFR
1200 – Local Area VFR
7500 – Unlawful interference
7600 – Radio failure
7700 – Emergency

Local Frequencies
North Shore	118.0
Emergency	121.5
Kaipara/Parakai	119.1
Gulf/City	120.4
Whenuapai ATIS	128.3
Whenuapai TWR	134.5
Auckland ATIS	127.8
Auckland TWR	118.7

Emergencies
Refer to Operating Handbook
Engine fire at start
Starter : engage
Mixture : idle/cutoff
Throttle : full open
Fuel pump : off
Fuel selector : off

Engine fire in flight
Increase airspeed
Fuel pump off
Fuel selector off
Throttle closed
Mixture idle/cutoff
Magnetos off
Land ASAP

Smoke/Electrical fire
Master off
Electrical equipment off
Floor vents open
Cabin heat off
Land ASAP

Low oil Pressure
Land ASAP
Prepare for engine failure

High Oil Temperature
Mixture full rich
Land ASAP
Prepare for engine failure

Low fuel pressure
Fuel pump on
Fuel selector switch tanks
Check fuel pressure
Prepare for engine failure