Preflight & Preparation
Cabin / - canopy secure, clean / - controls unlocked, belts / - flight manual tech log, airworthiness cert, radio licence / - compass & card / - emergency equipment, ELT / - controls & trim free / - mags. Off, throttle closed / - fuel valve on / - master on, walk around, check lights & stall warning / - master off / Empennage / - fuel quantity, endurance / - fuel cap locked / - fuel drain – clear, no water, no dirt / - left static vent clear / - horizontal stabiliser free movement, surface clean / - rudder movement, surface clean / - tail section screws & cables / - external power door closed / Right Wing / - flap secure / - aileron free movement / - surfaces clean / - free of damage / - remove tie-downs, chocks / - main gear undamaged, tyre tread, brakes, oleo extension, spats secure	Nose / - cowl flap, check oil >4qts / - cowl secure / - exhaust secure / - windscreen clean / - nose wheel undamaged, tyre tread, oleo 50-80mm, spats secure / - air intakes clear / - prop & spinner clean / - alternator belt tight / Left Wing / - pitot tube clear / - main gear undamaged, tyre tread, brakes, oleo extension, spats secure / - surfaces clean / - free of damage / - remove tie-downs, chocks / - aileron free movement / - flap secure	Passenger Brief / - Emergency equipment location & use : ELT, extinguisher, first aid, axe / - Outside : keep behind wings, clear of prop / - Cabin entry & exit / - Canopy emergency release / - Headset, use of radio push to talk / - Stowage pockets, airsick bags / - Seats, belts (always secure) / - Keep clear of controls – stick, rudder / - Lifejacket use if equipped / - Assist with traffic lookout / - Notify pilot of dizziness, nausea, toilet, etc.

Takeoff / Holding point checks: / TMPFFIHCTR / Line-up checks: / RTLWDR / Full throttle, keep straight / Rotate 55 kts / Best angle climb 65 kts / Clean-up – flaps, fuel pump / Best rate climb 75 kts Precision Landing / Downwind checks / BUMFHW / Carb. Heat On / Throttle 1800rpm / Check white arc / Flaps 10, lookout, turn base / Throttle as required / Speed 75 kts / Turn Final / Full flaps 35°, 65 kts / Short final : carb heat off / Nose up to 60 kts / Max Performance Takeoff / Holding point checks / TMPFFIHCTR / Note +ve acceleration point / Note rotate point / Line-up checks / RTLWDR / Hold brakes / Throttle 2000rpm / Cycle Carb heat / Full throttle, min 2300rpm / Release brakes, keep straight / Begin Rotate 55kts / Best angle climb 60 kts / Clean-up – flaps, fuel pump / Best rate climb 75 kts / Cruise, Climb / Cruise 2400-2450rpm / Approx 95kts Speeds / Stall, full flap (Vs0) 48kts / Stall, clean (Vs1) 57kts / Best angle climb 65kts / Best rate climb 75kts / Best glide dist. 75kts / Max flap (Vfe) 97kts / Max Manoeuv. (Va) 129kts / Never Exceed (Vne) 155kts / Max crosswind 18kts / Transponder Codes / xxxx – Aircraft discreet code / yyyy – Flight plan assigned code / 1200 – Local Circuit / 1400 – Local Area / Landing / Downwind checks / BUMFHW / Carb. Heat On / Throttle 1800rpm / Check white arc / Flaps 10, lookout, turn base / Throttle as required / Speed 75 kts / Turn Final / Full flaps 35 / Speed 65 kts / Short final : carb heat off Local Frequencies / North Shore 118.0 / Emergency 121.5 / Kaipara/Parakai 119.1 / Gulf/City 120.4 / Whenuapai ATIS 128.3 / Whenuapai TWR 134.5 / Auckland ATIS 127.8 / Auckland TWR 118.7	Emergencies